## Slide 1: Bindings & Mappings between Two System Hierarchies
Peter Feiler
Jan 2016
Notes: Title Slide
  Title and Subtitle text blocks should not be moved from their position if at all possible.

## Slide 2: Bindings between System Hierarchies
AADL supports a (primary) containment hierarchy
Semantic connections represent flow between and within subtrees
Managed interaction complexity by requiring connections up and down the hierarchy to restrict arbitrary connectivity
Note: for subprogram calls we offer both a connection and a mapping specification
Deployment bindings are a mapping from elements of one subtree to elements of another subtree
The subtrees represent different system layers in a layered architecture with the lower layer typically representing resources to the higher layer
Bindings represent resource allocation
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 3: Binding Issues
Bindings are currently expressed by properties
Binding related properties are not distinguishable from others
  Properties that express bindings
  Properties that relate to bindings
EMV2 propagation paths are derived from bindings and binding points currently are identified by special keyword
Binding properties reach down the instance containment hierarchy
  A primary driver for introducing contained property associations

## Slide 4: Binding Specification Proposal
User-definable binding types
Introduce name and source/target model elements
Binding instances
  Deployment configuration
Binding points
Binding constraints, properties, propagation paths

## Slide 5: Binding Type
Define binding type
  User defined name, sets of source and target categories
  Binding ProcessorBinding : { thread, thread_group, process} -> { processor, virtual processor, system }
1-to-n binding Alternatives (*):
  example – multiple cores
  Binding MultiCoreBinding : { thread, thread_group, system } ->* { processor}
1-to-n binding Sequence (+):
  example – connection binding
  Binding to flows in the target architecture represents sequences
  Do we still need sequences here?
  Binding ProtocolBinding : { port_connection, virtual_bus } ->+ { bus, virtual_bus, system }
  Definitions placed in a container similar to property types in property sets

## Slide 6: Flows and Bindings
End-to-end flow & flow implementation across virtual and hardware platform elements
  Expressed by end to end flow declaration
Layered virtual buses
  Access connections between virtual buses (interconnected virtual channels)
  Flows across interconnected virtual buses
  Binding of connections to flows
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 7: Binding Instances
  Binding of unchangeable source and target hierarchies
  Declared as a configuration section
  Associated with component that contains both source and target subtrees
  Can be applied to implementations and configurations
    System AS.deploymentconfig configures AS.systemconfig
    Bindings
    -- single binding target
    ProcessorBinding : Appsys.sub.proc.thread1 -> platform.node.cpu1;
    ProcessorBinding : Appsys.sub.proc.thread2 -> platform.node.cpu2;
    -- multiple alternatives
    ProtocolBinding : Appsys.sub.proc.conn1 -> (platform.proto1, platform.proto2);
    -- sequence
    ProtocolBinding : Appsys.sub.proc.conn1 -> (platform.network.bus1 + platform.network.bus2);

## Slide 8: Partial and Nested Bindings
Partial binding configurations
  Partially configured source and target system
    Only for those elements that have been configured
  Subset of elements are bound
    Bindings cannot be overridden
Nested binding configurations
  Subsystem may be internally fully bound
  Configuration that includes binding has been configured in
Visibility of subcomponent hierarchy
  Configurable subsystems use prototype to hide internal hierarchy

## Slide 9: Endpoints of Bindings
Source and target of bindings are components
  They act as implicit binding points
  Binding type definition tells us which component categories require binding declarations
Constraints on bindings
  In V2: Allowed_xxx_Binding_Class and Allowed_xxx_Binding on source of binding
  V3 options
    Property: Allowed_binding_Class => xxx applies to <component>.<bindingtype>
      Implicit binding point via binding type
      Property applies to source of binding
      How to express property on target of binding?
    Via binding types that limit endpoints to specific component classifiers
    Via constraint language

## Slide 10: Properties on Bindings
Properties on bindings
  On binding point
  On binding
    Should bindings have names like connections?

## Slide 11: Bindings and EMV2
In EMV2 binding related propagation points are identified by
  Special keywords (V2)
    For sources: processor, memory, connection, binding,
    For targets: bindings (all bindings with component as target)
  the binding type name (V3)
    In/out indicates direction of propagation: could be from source to target or vice versa
    Components involved as source in one binding and destination in another binding of same type
      Virtual processor is both source and target of processor binding
      As source and as target it can be on the outgoing and incoming end of propagations

## Slide 12: Named Binding Instances
Names on binding instances to be able to associate property values with each instance
    System AS.deploymentconfig configures AS.systemconfig
    Bindings
    -- similar to connection declarations
    PB1: ProcessorBinding Appsys.sub.proc.thread1 -> platform.node.cpu1;
    PB2: ProcessorBinding Appsys.sub.proc.thread2 -> platform.node.cpu2;

## Slide 13: Explicit Binding Point Definition
Explicit in features section:
  Identifies source or target of binding
  optional classifier(s) restrict the type of target
  Virtual bus proto1
  features
  RequiredProtocols: Requires binding ProtocolBinding [ VBOrBusClassifier ];
  ProvidedService: Provides binding ProtocolBinding [ VBOrBusClassifier ];
  Binding related properties
    Properties are currently on the component being bound or the target
      Separate properties for each of the binding types
    Properties on binding points
      Number of acceptable binding sources
      Subset of resource capacity available through binding point