## Slide 1: Model Driven Engineering with Capella and AADL Bassem Ouni, Pierre Gaufillet, Eric Jenn, Jérôme Hugues

## Slide 3: Introduction
Projects INGEQUIP and MOISE at IRT Saint Exupéry
INGEQUIP
  Co-development agility to assist Equipment design
  An activity focused on HW-SW Co-design
  Applies methods and tool on large demonstrator
    Mobile vehicle or Rover TwIRTee
MOISE
  MOdels and Information Sharing for System engineering in Extended enterprise
  From document-based specification process to model-driven specification process
  Ensure multi-view system design and verification in a heterogeneous context
  Collaborative engineering processes and methods in a regulation (“certification”)

## Slide 4: Why Capella to AADL?
Capella is positioned on the most abstract part of the system development while AADL doesn’t offer operational or system analysis
AADL goes further than Capella in terms of detailed architecture with explicit hardware components – device, processor, memory, bus – and explicit software components – process, thread, subprogram.
Operational Analysis
System Analysis
Logical architecture
Physical architecture
Abstract architecture
Detailed architecture
Behavioral model
Error model
Abstraction level
Capella
AADL

## Slide 5: Target chain
System Functional breakdown
System Logical architecture
System Physical Architecture
Preliminary Software Architecture
Software Architecture
Source code skeletons
Distributed Application Framework
Functional Source code
Arcadia
AADL
Refinement
Generation
Allocation
Allocation
Generation
Manual
Completion
Applications
IP-XACT

## Slide 6: Target chain
System Functional breakdown
System Logical architecture
System Physical Architecture
Preliminary Software Architecture
Software Architecture
Source code skeletons
Distributed Application Framework
Functional Source code
Capella
AADL
Refinement
EMF, Acceleo, Java
Allocation
Allocation
OCARINA
Manual
Completion
Applications
IP-XACT tree editor
VLAB
Space Studio

## Slide 7: TwIRTee Functional Breakdown

## Slide 8: TwIRTee Logical Architecture

## Slide 9: TwIRTee Physical Architecture

## Slide 10: System architecture with Capella
Modelling conventions
  Physical architecture breakdown stops when a leaf is allocated to hardware – device - or software – application.
  Flows are neither typed nor constrained
  Interconnected ports implicitly define a bus
  Software is allocated to CPUs and logical flows to physical flows
  System functions are not used

## Slide 11: Capella to AADL mapping

## Slide 12: Extraction of Bus
PC1
PC1.1
PC1.2
PC1.1.1
PC2
PC2.1
PL1
PL2
PL3
-Gathering groups of physical links which are connected to each other.
-Each group will be mapped in a physical bus (Physical component with Bus port).
-Connected Physical Links are translated into requires access connectors to a bus
through intermediate ports.
PP1
Bus 1
Bus 2
PC: Physical component
PL: Physical link
PP: Physical port

## Slide 13: Extraction of Bus
PC1
PC1.1
PC1.2
PC1.1.1
PC2
PC2.1
PL1
PL2
PL3
PP1
Bus 1
Bus 2
-Synthetic links and synthetic ports are generated=> mapped to AADL connections and requirements of bus accesses.
-Considering the architecture as a tree, we first search the external ports (Last level of the tree).
-Bus ports are connected to external ports.
1
2
3
4
6
5
7
8
9
10

## Slide 14: Extraction of logical connections
Components exchanges are translated into oriented abstract flows through intermediate ports.

## Slide 15: Preliminary Software Architecture with AADL
Fully generated from Capella
Read-only artefact – Regeneration is straight-forward

## Slide 16: Software Architecture with AADL
Inherits from the preliminary architecture
Refined manually by adding
  Internal application objects: tasks, buffers, semaphores, etc.
  Typed flows
  Static software architecture: application subsets, API
  Real Time constraints
  Abstract behaviour
Impacts of modification in the preliminary architecture are easily identified thanks to inheritance and refinement relationships.
Can be used for formal behavior verification

## Slide 17: Software Architecture with AADL

## Slide 18: Software Architecture with AADL
Validation with AADL inspector
  Structural properties
  Scheduling with Marzhin and Chedar (TBD)

## Slide 19: Distributed applications Framework with PolyORB
OCARINA generates code skeletons for each application from the software architecture in AADL including:
  Tasks management
  Synchronization/Communication glue
The generated code relies on a distributed application framework: PolyORB HI (C, ADA)
The functional code is completed by hand

## Slide 20: Capella2AADL in brief
Role
  Initializes hardware/software design from system physical architecture
Job done
  AADL analysis and meta-modeling
  AADL Prototyping
  Experimentation on TwIRTee
Issues
  Multiplexed communications needed in AADL not supported by Capella
Limitations
  Global transformation only – Subsets not supported
Capella to AADL Roadmap
  Support transparent components on physical flows – transceivers, routers, etc.
  Improved naming – ports, flows, etc.
Open the door to better exchanges of information between system and software engineers

## Slide 21: Questions ??? Thanks a lot for your attention