## Slide 1: Composition of Interfaces
Software Engineering Institute
Carnegie Mellon University
Pittsburgh, PA 15213
Peter Feiler
Jan 2016
Notes: Title Slide
  Title and Subtitle text blocks should not be moved from their position if at all possible.

## Slide 2: Composition of Interfaces
Objectives
  Composition of interfaces and properties into a component type
  Single connection declaration for interfaces
  Composition rules for features, modes, flows, annexes
Approach
  Allow extends of multiple component types
  Composition rules align with current extends rules
    Composition of abstract category to become abstract or specific component category
    Composition of specific component category into the same category
  Allow multiple named instances of the same interface
    Effectively offers nested feature group connectivity

## Slide 3: Composition of Interfaces
Features accessible directly within namespace of component
  Externally: connections identify subcomponent and feature (V2)
  Internally: connections identify feature (V2)
Abtract Logical
temperature: out data port;
Speed: out data port;
End Logical;
Abstract Physical
Network: requires bus access CANBus;
End Physical;
System s1 extends Logical
Features
Onemore: out event port;
End s1;
System s2 extends Logical, Physical
End s2;
System s3 extends Logical, Physical
Features
Onemore: out event port;
End s3;
V3: Features from Logical, Physical and local cannot be in conflict.
V3: Feature names from Logical and Physical cannot be in conflict
V2: Locally added feature name cannot be in conflict with Logical features
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 4: Composition of Directional Interfaces
Interfaces with directional features may be included as original direction or as inverse direction for component at the other end of a connection
  This is the inverse of from feature groups
System Sender extends Logical, Physical
End s1;
System Receiver extends inverse of Logical, Physical
End s2;
inverse of for Logical to get opposite port direction
No inverse of for Physical since both require access to physical platform
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 5: Composition of Named Interfaces
Objective: Handle multiple instance of same interface, e.g., voter taking input from multiple instances of same subsystem
Individual features qualified by interface instance name
  Internally: interfacename . Featurename
  Exernally: subcomponentname . Interfacename . Featurename
System sif1 extends
IFlog: Logical,
IFphys: Physical
End sif1;
System voter Extends
if1: inverse of Logical,
if2: inverse of Logical
End s2;
System implementation Top.impl
Subcomponents
Sub1: system sif1;
Sub2: system sif1;
Voter: system voter;
Connections
Conn1: Sub1.IFlog -> Voter.if1 ;
Conn2: Sub2.Iflog.temperature -> Voter.if2.temperature ;
Connections between named interfaces (aka feature group connections) or between features in an interface (reachdown)
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 6: Composition of Named Interfaces
Objective: Handle interfaces with conflicting feature names
Abtract Logical1
temperature: out data port;
Speed: out data port;
End Logical;
Abstract Logical2
temperature: out data port;
weight: out data port;
End Logical2;
System s2 extends L1: Logical1, L2: Logical2
End s2;
System implementation s2.i
Subcomponents
sub1: system s1;
Connections
conn1: sub1.out -> L1.temperature;
conn2: sub1.out -> L2.temperature;
End 2s.i;
In the implementation the connection declarations specify that the same sub1 output is mapped into a port in two different interfaces. These may be ports with the same name, or ports with different names.
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 7: Nested Interfaces
Works for composition of named interface instances
Effectively we have nested feature groups
Deprecate feature groups in V3
Abstract composite extends L1: Logical1, PF: Physical
End composite ;
System Top extends FG: composite, L2: Logical2
End top;
Unnamed interfaces flatten the
Abstract composite extends Logical1, Physical
End composite ;
System Top extends composite, Logical2
End top;
All features in single namespace
Name conflict between L1 and L2 feature temperature
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 8: Interface Equivalence Mapping
Support for composition of independently developed subsystems or subsystem with different nested interface hierarchies
  Reusable equivalence mapping
  map1: mapping Type1 == Type2 as
  lfea1.fea2 == rfea1;
  Lfea1.fea3 == rfea2.fea11
  end mapping ;
  Inline mappings (reach down multiple nesting levels
  Conn1: sub1.lfea1.fea2 -> sub2.rfea1;
  Conn2: sub1.lfea1.fea3 -> sub2.rfea2.fea11;
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 9: Composition of Interface Properties
Interface properties are inherited by the component
  Also for nested interfaces the properties
  In feature groups the feature group type property did not become a component property but an inheritable property of the feature group
Abtract Logical
temperature: out data port;
Speed: out data port;
Properties
Myname => “peter”;
End Logical;
Abstract Physical
Network: requires bus access CANBus;
Properties
Hisname => “peter”;
End Physical;
System s2 extends Logical, Physical
End s2;
System s3 extends Logical, Physical
properties
Myname => “paul”;
End s3;
Cannot inherit same property from two interfaces: equal is ok
Can override property locally
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 10: Composition of Flows
Same rules as V2 extends
Flows in interfaces are only with respect to its features
The composite component may add flow specification for flows between features in different interfaces
Abtract Logical
temperature: out data port;
Speed: out data port;
flows
temp: flow source temperature;
End Logical;
System s2 extends Logical, Physical
End s2;
System s3 extends Logical, Physical
flows
spd: flow source speed;
End s3;
Cannot inherit flows with the same name. Use of named interfaces addresses possible name conflicts.
Can add flows for inherited features as was possible in V2
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language

## Slide 11: Composition of Modes
Only one source (same as extends of single classifier)
  Local additions as in V2
Union of mode states from different interfaces
  Were they developed independently for the same state machine or as independent state machines?
Separate mode state machines
  We currently do not support multiple concurrent state machines for the same component
  Note that modal subcomponents have the effect of concurrent state machines
Notes: Key points (Objectives of the Slide): What is covered in this section
Slide Content Description:
Presentation Script: We address the following subjects in this section
Modeling and embedded systems engineering
What is modeling?
What is Software Architecture?
Model * Engineering
Definition of terms – putting them in perspective
Motivation for model-based engineering
The AADL Language – We discuss:
That it is aStandard
Overview of the Language
Insight into how the language came to be – development pattern -New WG activities
We are presenting Version 2
Model-based Embedded systems engineering and the role of aadl (MBSE role of aadl)
Software and Systems Engineering
Focus of the SAE AADL
33-38
Definition and History of aadl
42 -43
AADL Language Overview
The grammar, syntax, and semantics
AADL tools
Extensions to the language